## Slide 1: Anomaly diagnosis method- Pre-Study
15.09.2023

## Slide 2: Content
Scenario
Key Idea
Model Workflow(Training and Inference)
Method
  CNN+LSTM
  TCN

## Slide 3: Scenario
Alarm report
observation from custmors
Technical Issue
RCA_Stage1
RCA_Stage2
Deviation detection
Which parameter is anomaly
Identifies underlying causes of faults.
Common Database
Choose the timeframe when the issue occurred.
EDDA
Get the abnormal parameter
Inference on EDDA
EDDA
Get the root cause of the issue(Probability)
User Behaviour
Process Stage
Eg:
Issue happened between 12/09/2023 9:00 am to 10:00 am
Select data between12/09/2023 9:00 am to 10:00 am
Eg:
BPT is diagnose anormal by EDDA
Eg:
Fuel nozzle clogging : 49%
Fuel gas composition change : 21 %
Fuel gas valve malfunction : 2%
Anomaly diagnosis will be applied here
Inference on EDDA

## Slide 4: Key Idea
Each abnormal case is a grey scale picture
Problem Define : Determine the corresponding root cause (output) for a given abnormal input
Aim : Build Time Series Classification model , each parameters has own classification model
Key idea: Each time series sequence is transformed into a 2D image-like representation.
  Pattern Recognition: By using a 2D image-like representation , we can uncover whether there are specific patterns within the time series that share the same root cause
  Temporal Relationships: study the relationships and patterns between different variables over time
Notes: We can address the fault diagnosis problem, a data-driven framework is proposed to model data from different fault classes and quantify fault diagnosis performance.
fault diagnosis problem regard as muti-classification problem, In the problem of abnormal subsequence detection
Assume that time series X = [x1, x2, . . . , xT ] is an
ordered set of values xi ∈ R, with T denoting the
length of the time series X. Also consider a dataset D =
{(X1, Y1), . . . ,(XN , YN )} to be a collection of pairs (Xi
, Yi)
where Xi
is a time series with Yi as its corresponding
label. TSC then consists of designing a classifier on D in
order to map from the raw feature space X to a probability
distribution over the set of unique classes in D
For time series classification in a supervised setting where all of the data has class labels,
, a time series is nothing more than a two-dimensional numpy array with its first dimension corresponding to the time axis and the second one being the feature dimensionality (1 by default).
#
Donation:
T=[𝑇_(1,) 𝑇_(2,) 𝑇_(3,)…𝑇_(𝑛,) ]with n denoting the length of length of the time series T. Also consider a dataset D={(𝑇_(1,),𝑌_(1,) ),(𝑇_(2,),𝑌_(2,) )….(𝑇_(𝑛,),𝑌_(𝑛,) )} is one
For instance, consider a two-dimensional matrix where 'n' represents the length of the time series and 'm' serves as a parameter associated with BPT (Behavior Pattern Analysis). We can categorize specific events as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
Suppose we encounter a fuel nozzle clogging issue within the time frame of 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
[Two-Dimensional Matrix] → Class 1
This formulation maintains proper grammar and flow.
Let's assume a two-dimensional matrix where 'n' represents the length of the time series, and 'm' stands for the number of variables associated with irregularity.
Now, consider an incident where a fuel nozzle clogging issue occurred between 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
In the context of this two-dimensional matrix, the occurrence would be classified as Class 1.
This text has been refined for better grammar and clarity.
Time series classification is a machine learning task that involves categorizing or labeling time series data into predefined classes or categories. In this task, the input data consists of time-ordered sequences of observations, and the goal is to assign a class label to each time series based on its patterns, trends, or characteristics.

## Slide 5: Model Workflow
Data preparing and pre-process
Aim to build Time Series Classification model : Each parameters has own classification model
Feature Engineering:
  Extract domain-specific attributes, following traditional detection criteria; expert guidance is essential.
E.g. BPT is abnormal parameters,{X1,X2…X7} is variable related with BPT
interval for the occurrence of the issue
Notes: We can address the fault diagnosis problem, a data-driven framework is proposed to model data from different fault classes and quantify fault diagnosis performance.
fault diagnosis problem regard as muti-classification problem, In the problem of abnormal subsequence detection
Assume that time series X = [x1, x2, . . . , xT ] is an
ordered set of values xi ∈ R, with T denoting the
length of the time series X. Also consider a dataset D =
{(X1, Y1), . . . ,(XN , YN )} to be a collection of pairs (Xi
, Yi)
where Xi
is a time series with Yi as its corresponding
label. TSC then consists of designing a classifier on D in
order to map from the raw feature space X to a probability
distribution over the set of unique classes in D
For time series classification in a supervised setting where all of the data has class labels,
, a time series is nothing more than a two-dimensional numpy array with its first dimension corresponding to the time axis and the second one being the feature dimensionality (1 by default).
#
Donation:
T=[𝑇_(1,) 𝑇_(2,) 𝑇_(3,)…𝑇_(𝑛,) ]with n denoting the length of length of the time series T. Also consider a dataset D={(𝑇_(1,),𝑌_(1,) ),(𝑇_(2,),𝑌_(2,) )….(𝑇_(𝑛,),𝑌_(𝑛,) )} is one
For instance, consider a two-dimensional matrix where 'n' represents the length of the time series and 'm' serves as a parameter associated with BPT (Behavior Pattern Analysis). We can categorize specific events as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
Suppose we encounter a fuel nozzle clogging issue within the time frame of 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
[Two-Dimensional Matrix] → Class 1
This formulation maintains proper grammar and flow.
Let's assume a two-dimensional matrix where 'n' represents the length of the time series, and 'm' stands for the number of variables associated with irregularity.
Now, consider an incident where a fuel nozzle clogging issue occurred between 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
In the context of this two-dimensional matrix, the occurrence would be classified as Class 1.
This text has been refined for better grammar and clarity.
Time series classification is a machine learning task that involves categorizing or labeling time series data into predefined classes or categories. In this task, the input data consists of time-ordered sequences of observations, and the goal is to assign a class label to each time series based on its patterns, trends, or characteristics.

## Slide 6: Model Workflow
Data preparing and pre-process
Label data :
  Supervised learning
  each abnormal case can be represented as a two-dimensional matrix, and each matrix can be associated with a label
  Label provide from experts
Normalization
Assume a with ‘n’ represents the length of the time series and 'm' stands for the number of variables associated with abnormal parameters.
where i represents an abnormal case. We can consider a dataset }, where is a time series with Yi as its corresponding label.
E.g.
BPT : Fuel nozzle clogging issue happened between12/09/2023 9:00 am to 10:00 am ,this can be represented as follows:
Fuel nozzle clogging → class 1
Fuel gas composition change → class 2
Fuel gas valve malfunction → class 3
→ class 1
12/09/2023 10:00
12/09/2023 9:00
to
Aim to build Time Series Classification model : Each parameters has own classification model
Notes: We can address the fault diagnosis problem, a data-driven framework is proposed to model data from different fault classes and quantify fault diagnosis performance.
fault diagnosis problem regard as muti-classification problem, In the problem of abnormal subsequence detection
Assume that time series X = [x1, x2, . . . , xT ] is an
ordered set of values xi ∈ R, with T denoting the
length of the time series X. Also consider a dataset D =
{(X1, Y1), . . . ,(XN , YN )} to be a collection of pairs (Xi
, Yi)
where Xi
is a time series with Yi as its corresponding
label. TSC then consists of designing a classifier on D in
order to map from the raw feature space X to a probability
distribution over the set of unique classes in D
For time series classification in a supervised setting where all of the data has class labels,
, a time series is nothing more than a two-dimensional numpy array with its first dimension corresponding to the time axis and the second one being the feature dimensionality (1 by default).
#
Donation:
T=[𝑇_(1,) 𝑇_(2,) 𝑇_(3,)…𝑇_(𝑛,) ]with n denoting the length of length of the time series T. Also consider a dataset D={(𝑇_(1,),𝑌_(1,) ),(𝑇_(2,),𝑌_(2,) )….(𝑇_(𝑛,),𝑌_(𝑛,) )} is one
For instance, consider a two-dimensional matrix where 'n' represents the length of the time series and 'm' serves as a parameter associated with BPT (Behavior Pattern Analysis). We can categorize specific events as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
Suppose we encounter a fuel nozzle clogging issue within the time frame of 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
[Two-Dimensional Matrix] → Class 1
This formulation maintains proper grammar and flow.
Let's assume a two-dimensional matrix where 'n' represents the length of the time series, and 'm' stands for the number of variables associated with irregularity.
Now, consider an incident where a fuel nozzle clogging issue occurred between 12/09/2023, from 9:00 am to 10:00 am. This can be represented as follows:
Fuel Nozzle Clogging → Class 1
Fuel Gas Composition Change → Class 2
Fuel Gas Valve Malfunction → Class 3
In the context of this two-dimensional matrix, the occurrence would be classified as Class 1.
This text has been refined for better grammar and clarity.
Time series classification is a machine learning task that involves categorizing or labeling time series data into predefined classes or categories. In this task, the input data consists of time-ordered sequences of observations, and the goal is to assign a class label to each time series based on its patterns, trends, or characteristics.

## Slide 7: Model Workflow
Training unit : An abnormal case
Data balance or not
  Balance : Random Sample. 7:3 or 8:2 to split training set and testing set
  Unbalance : SMOTE
Model Training
Method
  CNN+LSTM
  TCN
The model's output will consist of probabilities assigned to each class.
Model Evaluate
Primary concern is accuracy
  The formula for multi-class classification accuracy
  Number of Correctly Classified Instances : the total number of instances correctly assigned to their respective classes by the model.
  Total Number of Instances : the complete dataset size, including all classes.
precision, recall, F1-score, confusion matrices
Cross-validation
.
.
.
.
.
.
BPT fault dataset
Class 1 (Fuel nozzle clogging) : 49%
Class 2 (Fuel gas composition change) : 21 %
Class 3 (Fuel gas valve malfunction) : 2%
Data sampling
Aim to build Time Series Classification model : Each parameters has own classification model
Notes: Let's get into the training and evaluation phase of our time series classification model.
Our training unit, in this case, we also considern our dataset whether it's balanced or not. If we have a balanced dataset, meaning each class is fairly represented, we can use a straightforward random sample split. Common ratios include 70% training and 30% testing or 80% training and 20% testing.
However, in cases of data imbalance, where some classes have significantly fewer examples, there a technique called SMOTE, or Synthetic Minority Over-sampling Technique. SMOTE helps us address the imbalance issue by creating synthetic samples for minority classes, thereby achieving a more balanced dataset.
Now, let's talk methods. We've considered two approaches for our time series classification:
𝑁𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝐶𝑜𝑟𝑟𝑒𝑐𝑡𝑙𝑦 𝐶𝑙𝑎𝑠𝑠𝑖𝑓𝑖𝑒𝑑 𝐼𝑛𝑠𝑡𝑎𝑛𝑐𝑒𝑠
1. CNN+LSTM:
2. TCN (Temporal Convolutional Network):
those two method i will explain more detail in next sildes
When it comes to model output, we're assigned probabilities assigned to each class. actaully In classification models, the output layer's neuron values represent probabilities for each class, especially when using softmax.
Our primary metric is accuracy, which represents the proportion of instances each class is classified correctly. The formula is provided below. It's calculated by dividing the number of correct predictions by the total number of . We also CAN assess precision, recall, F1-score, and examine confusion matrices to gain deeper insights into model performance. ALSO cross-validation
From here, this might seem a bit confusing. From a developer's perspective, the primary goal is to maximize the prediction accuracy of the model. We often approach this as we do with standard classification models: each input is assigned to a single predicted outcome, and the aim is for every prediction to be correct. However, for the users, we want to help them gain insights into the probabilities of various potential causes for a given issue. Thus, we hope we can predict correctly, especially for the cause with the highest probability. Presenting results using this probabilistic method provides users a degree of flexibility in interpretation.

## Slide 8: Method-CNN+LSTM
Feature Extraction with CNNs
LSTM for Sequential Learning
+
Long-term Recurrent Convolutional Networks for Visual Recognition and Description https://arxiv.org/pdf/1411.4389.pdf
CNN-LSTM Deep Learning Architecture for Computer Vision-based Modal Frequency Detectio
A Hybrid CNN-LSTM Based Approach for Anomaly Detection Systems in SDNs https://dl.acm.org/doi/fullHtml/10.1145/3465481.3469190

## Slide 9: Method-TCN
The description of a Temporal Convolutional Network is based on the following paper:An Empirical Evaluation of Generic Convolutional and Recurrent Networks for Sequence Modeling https://arxiv.org/pdf/1803.01271.pdf
Architecture: 1D fully connected layers and convolutional layers. These convolutional layers utilize causal and dilated convolution
Causal Convolution:
  Extract derived features from time series data
  ensure that at any time t, the model is only using information from time t and earlier.
  In practice, it's like applying a 1D convolutional layer, but with padding on the left, ensuring that the output at time t does not look into the future.
Dilated Convolution:
  Receptive Field Size: As you move up the layers, convolution window size grows, thereby increasing the receptive field and reducing computation.
Residual Block: Each residual block contains
  A causal convolution.
  ReLU activation function.
  A causal convolution.
  ReLU activation function.
  A skip connection that adds the input to the block to its output.
  If the input and output dimensions don’t match, a 1x1 convolution is used to transform the input before adding.
  Stacking Residual Blocks:
  Multiple such residual blocks are stacked to increase the receptive field of the network.
  The depth of TCN (i.e., the number of these stacked residual blocks) determines how far back in the input sequence model can effectively "see" or consider.
Output Layer:
  After all the residual blocks, we can attach an output layer suitable for our task. For our sequence classification is the entire sequence gets a single label,the output might be a softmax distribution over classes for the entire sequence.

## Slide 10: Method-TCN
The description of a Temporal Convolutional Network is based on the following paper:An Empirical Evaluation of Generic Convolutional and Recurrent Networks for Sequence Modeling https://arxiv.org/pdf/1803.01271.pdf
(A) Overall architecture of the TCN-based model.
(B) Architecture of a residual block

## Slide 11: Method- Implemented
  CNN+LSTM
  Convolutional layers (using tf.keras.layers.Conv1D for time series)
  LSTM layers (using tf.keras.layers.LSTM).
  can stack these layers sequentially in a model
  TCN
  TensorFlow does support 1D convolution which is essential for TCN, it doesn't provide an out-of-the-box TCN layer. However, there are third-party implementations, such as the keras-tcn package
Can be implemented using TensorFlow