## Slide 1: Cracked Rotor Prediction-Initial study
27.10.2023

## Slide 2: Content
Background
Problem Define
Rule of detection
Project Scope

## Slide 3: Background
Reason : The consequences of shaft cracks are catastrophic, like operational damages, replacement costs, lost revenues
making prevention and early detection crucial for our sustainability and profitability.

## Slide 4: Define Problem
What problem do we want to address with data?
. Early fault detection
Condition monitoring
Fault Diagnostic
Multi-fault diagnostic

## Slide 5: Binary Classification : Evaluation
Since our data is imbalance
Using Precision-Recall Curve to evaluate binary classification model
  The PR curve illustrates the trade-off between precision and recall for different threshold values. This makes it particularly useful for imbalanced datasets because it focuses only on the positive class
Find the optimal threshold base on maximum Precision-Recall Curve value
  Bias Towards the Majority Class : setting a threshold of 0.5 might not capture the true distribution and characteristics of the data.
Evaluation methods:
(1,1) is the best

## Slide 6: Binary Classification : Model Comparison
Cnn_TL_baseline | Predicted | 
Actual | 4738 | 3
 | 1 | 50
Optimal threshold: 0.24912743 |  | 
Cnn_TL_Class_Weight | Predicted | 
Actual | 4739 | 3
 | 2 | 49
Optimal threshold: 0.8662481 |  | 
FCN_baseline | Predicted | 
Actual | 4737 | 5
 | 4 | 47
Optimal threshold:0.3874237 |  | 
FCN_Class_Weight | Predicted | 
Actual | 4739 | 3
 | 2 | 49
Optimal threshold: 0.97072464 |  | 
Model Name | F1_Score | False Positives Rate | False Negatives Rate
Cnn_TL_baseline | 0.9996 | 0.0196 | 0.0006
Cnn_TL_Class_Weight | 0.9995 | 0.0392 | 0.0006
FCN_baseline | 0.9991 | 0.0784 | 0.0011
FCN_Class_Weight | 0.9995 | 0.0392 | 0.0006
Analysis: (Depends on primary concern )
  Minimizing False Negatives: Models with class weights perform slightly better, particularly `Fcn_class_weight` and `Cnn_class_weight`.
  Minimizing False Positives: Cnn_TL_baseline is the best model as it as the lowest FPR of 0.0196
  Balance between the two rates is desired: `Cnn_baseline` offers the best balance with the highest F1 score and low FPR.
  While using class weights tends to improve the performance in the case of false negatives .the `Cnn_baseline` model (without class weight) still emerges as the most balanced and best-performing model across the board.
Notes: In conclusion, class weights appear to be effective in this situation, especially when our priority is to reduce false negatives.
However, it's essential to adjust our approach based on the specific requirements of our application.for example, As discussed this morning, false positives require greater attention in rotor craker detection.

## Slide 7: Sampling trial
Using different sampling method to solving imbalance class issue
Oversampling — Duplicating or Generate samples from the minority class
  Method 1: SMOTE- Base on KNN to generate the minority class data point (from imblearn.over_sampling import SMOTE)
  Method 2 : Interpolate
    Set the 'Timestamps' column as the index.
    Filter rows where 'predicted' is 1.
    Check differences between consecutive timestamps that satisfy step 2. If the difference is one minute, insert rows at 10-second intervals and interpolate.
Undersampling — Deleting samples from the majority class
  Method: Base on K-means clustering result ,then processing proportional sampling.
  Goal is to sample representative data points from the majority class.
    Apply k-means clustering to the majority class.
    Sample proportionally from each cluster. For instance, if one cluster is bigger (has more data points) than others, take more samples from it#
  Benefits :Representative Sampling and Preservation of Information , decrease training time
Notes: - **Representative Sampling**: By clustering first and then sampling, you ensure that the samples you retain are representative of the overall distribution of the majority class.
- **Preservation of Information**: Even though you're reducing the number of samples, by selecting from clusters you're ensuring that the "essence" or "major patterns" of the majority class are retained.

## Slide 8: Sampling trial – Undersampling(Kmeans + proportional sample)
Original positive class in train data : 11036
Undersampling positive class in train data : 5000
Undersampling will only be applied to the positive class in the training data
Raw Data
Training Data
Testing Data
Normalization & Windows sliding
Clean Data

## Slide 9: Sampling trial - Undersampling